## Slide 1: Collision Repair: Introduction and Careers
Chapter 1
Notes: 1

## Slide 2
FIGURE 1-1 During a major collision, like this head-on crash
test, tremendous energy is dissipated into the body/frame structures of both cars.
Notes: 2

## Slide 3: Objectives
Describe what happens to a motor vehicle during a collision
Summarize the basic steps needed to repair a vehicle damaged in an accident
Explain the major work areas of a typical collision repair facility
Summarize the work flow through a typical body shop
Notes: 3

## Slide 4: Objectives (continued)
Describe the types of positions or jobs available in the collision repair industry
Identify the setup and inner workings of a typical collision repair shop
Answer ASE-style review questions relating to collision repair
Understand fundamental terms used in the collision repair industry
Notes: 4

## Slide 5: Introduction
Auto body repair is also called collision repair
Collision repair skills are in high demand
Body shops do $10 billion of repair work per year
Only highly skilled, knowledgeable professionals can properly repair today’s vehicles
Notes: 5

## Slide 6: What Is Collision Repair?
Collision
  Damage caused by an impact (hit) on the vehicle
Head-on collision
  Two vehicles driving toward each other accidentally collide
  Often the worst type of accident
Auto body repair or collision repair
  Involves fixing a vehicle damaged in an accident
Notes: 6

## Slide 7
FIGURE 1-2 If the accident results in major damage and the vehicle cannot be driven, a wrecker is called to tow the car.
Notes: 7

## Slide 8: Accident Scene
Accident report
  Summarizes what happened during collision
  Lists information about drivers, their vehicles, and their insurance companies
Wrecker
  Truck equipped with special lifting equipment for raising and transporting damaged vehicle
Salvage yard
  Business that resells parts from collision damaged vehicles
Notes: 8

## Slide 9: Body Shop
Collision repair facility (body shop)
  Has well-trained technicians, specialized tools, and heavy equipment for restoring damaged vehicles to their pre-accident condition
Independent body shop
  Owned and operated by a private individual
Franchise body shop
  Tied to corporate headquarters that regulates and aids operation of the shop
Notes: 9

## Slide 10
FIGURE 1-3 The modern body shop is equipped with specialized
equipment and well-trained personnel. It can be a safe and enjoyable
place to work if safety rules are followed. If not, it can be a very
dangerous place!

## Slide 11: Body Shop (continued)
Dealership body shop
  Owned and managed under guidance of a new car dealership, such as General Motors, Chrysler, Lexus, etc.
Progression or production shop
  Assembly line organization with specialists in each area of repair
Specialty shop
  Performs only specific types of repairs
Notes: 11

## Slide 12: Damage Estimating
Damage estimate
  Prepared to calculate cost of repairs
  Labor, parts, and materials must be added to find total cost of repair
Estimator
  Makes an appraisal of vehicle damage
  Determines what must be done to repair the vehicle
Notes: 12

## Slide 13: Body Shop Repairs
Repair order
  Summary of repair instructions
  Repairs are carried out according to these instructions
Washup
  Thorough cleaning of vehicle with soap and water
  Followed by wiping body down with wax-and-grease remover
Notes: 13

## Slide 14
FIGURE 1-7 Before starting repairs, body shops usually wash the vehicle thoroughly to remove road dirt.
Notes: 14

## Slide 15: Body Shop Repairs (continued)
Metalworking areas
  Shop locations where damaged parts are removed, repaired, and installed
  Used for most collision repair tasks
Vehicle measurement: helps determine extent and direction of major damage
Frame/unibody straightening equipment
  Large steel framework, large steel towers, pulling chains, and hydraulic rams to pull frame or body back into its original position
Notes: 15

## Slide 16
FIGURE 1-8 To start work, you must normally remove damaged outer body parts to gain access to hidden parts that require straightening or replacement. Here the technician is removing a front fender.

## Slide 17
FIGURE 1-12 Constantly measure as you pull out damage. Here the tram gauge has been set to vehicle specs and compared to reference points on the damaged vehicle.
Notes: 17

## Slide 18: Body Shop Repairs (continued)
Panel replacement
  Removing panel or body part that is too badly damaged to be fixed
Panel straightening
  Using various hand tools and equipment to force damaged panel back into its original shape
Paint preparation
  Fine sanding and cleaning to prepare surfaces for refinishing process
Notes: 18

## Slide 19
FIGURE 1-15 You must restore corrosion protection to all repair
panels. Various products are available to prevent corrosion or rusting of new panels.

## Slide 20
FIGURE 1-17 A technician replaces a small air bag located on
the inside of the door frame. Note how the technician stays to one
side in case the air bag accidentally deploys. Air bags deploy with a
“bang” and can cause injury to your arms, hands, and face.

## Slide 21
FIGURE 1-18 Note the basic steps for removing a dent from a metal part. (A) Often panels have minor damage that can be repaired. (B) When a dent cannot be hammered out from inside the panel, a nail weld gun can be used. (C) With pull pins welded into the dent, attach a puller to each pin for forcing out the low spot. (D) After pulling damage, cut and grind off the pins until they are almost flush with the panel surface.
Notes: 21

## Slide 22
FIGURE 1–19 Body filler is commonly needed to smooth and level metal that has been straightened. (A) Mix body filler and hardener in correct proportions. (B) Apply the body filler to the clean body surface right away. (C) As soon as filler starts to solidify, use a coarse “cheese grater” file to rough out the shape. (D) After grating the filler, use an air sander and coarse grit sandpaper to cut the filler down more.
Notes: 22

## Slide 23
FIGURE 1-22 Self-etch or epoxy primer must be sprayed over all bare metal to bond to the metal. Primer-surfacer is often sprayed over body filler and the repair area to help level the repair area. Allow each coat of primer to flash properly before applying the next coat.

## Slide 24: Body Shop Repairs (continued)
Mixing room or mixing lab
  Power-ventilated area where refinish materials are mixed and prepared for application
Refinishing or repainting
  Steps needed to properly restore the vehicle’s finish or paint
Drying
  Using different methods to cure fresh paint
    Air drying-allows the paint to dry naturally
    Forced drying-uses equipment to accelerate cure
Notes: 24

## Slide 25
FIGURE 1-25 Most large body shops have their own paint mixing room.
It has all color pigments and other ingredients for mixing paint materials. Mixing rooms also have forced ventilation to prevent buildup of paint fumes.

## Slide 26
FIGURE 1-29 Excellent hand-eye coordination and specialized knowledge is needed to be a professional painter. (A) When painting a vehicle, keep the gun the correct distance from the surface. Also keep the gun parallel with the surface. Hold the air hose so it cannot touch and damage the wet paint. (B) When painting, try to move the spray gun smoothly and evenly. Use straight line paint strokes that overlap evenly.
Notes: 26

## Slide 27: Body Shop Repairs (continued)
Post-painting operations
  Removing masking tape, reinstalling parts, and cleaning vehicle
Mechanical repairs
  Tasks such as replacing damaged water pump, radiator, or engine bracket
Electrical repairs
  Tasks such as repairing severed wiring, replacing engine sensors, and scanning for computer or wiring problems
Notes: 27

## Slide 28: Complete Collision Services
Many body shops offer complete collision services
  Wheel alignment
  Cooling system repairs
  Electrical repairs
  Suspension repairs
  Air-conditioning repairs
  Glass replacement
Notes: 28

## Slide 29: Auto Body Careers
Auto body technicians must have basic skills in the following areas:
  Metalworker
  Welder
  Auto mechanic
  Sculptor
  Plumber
  Electrician
  Air-conditioning technician
  Computer technician
Notes: 29

## Slide 30: Auto Body Careers (continued)
Specialized technicians
  Metalworking technicians
  Refinish technicians
  Helpers
Other collision repair personnel
  Shop owner
  Shop supervisor
  Parts manager
Notes: 30

## Slide 31: Auto Body Careers (continued)
Other collision repair personnel (continued)
  Bookkeeper
  Office manager
  Receptionist
  Tow truck operator
Notes: 31

## Slide 32: Auto Body Careers (continued)
Other careers in the collision repair field
  Insurance adjuster or appraiser
  Vocational/technical instructor
  Salvage yard technician
  Dealership parts counterperson
  Paint company representative
  Auto manufacturer representative
  Equipment salesperson
Notes: 32

## Slide 33
Summary
A collision, nicknamed a crash or a wreck, is damage caused by an impact (hit) on the vehicle.
Auto body repair, also called collision repair, involves fixing a vehicle that has been damaged in an accident. The vehicle is first brought into the shop, where a damage estimate is prepared to calculate the cost of repairs.
Minor body damage only requires that a few parts be replaced or repaired before the car is repainted. Major body damage usually must be corrected by replacing, repairing, and straightening large body parts before repainting. A collision can also be severe enough to cause a total loss, where repairs would be more expensive than buying another car.

## Slide 34
Summary
Repair instructions are summarized on a printed repair order (RO), and the repairs are carried out according to those instructions. The metalworking areas are shop locations where damaged parts are removed, repaired, and installed. A stall is a work area for one vehicle, often marked off with painted lines on the floor.
Vehicle measurement is done to determine the extent and direction of major damage. Measurement systems are specialized tools and equipment that help the technician to check and measure for frame or body misalignment resulting from a high-impact collision.

## Slide 35
Summary
Frame straightening equipment (also called a frame rack) uses a large steel framework, pulling chains, and hydraulic power to pull or force the frame or body back into its original position.
A panel is a large metal or plastic body part-a fender, hood, truck, or roof panel, for example. Structural panel replacement involves welding a new panel in place of an old, damaged one. Panel adjustment involves moving or shifting a part to properly align with other parts or panels. When parts are replaced, corrosion protection coatings must be applied to prevent the new parts from rusting.

## Slide 36
Summary
Panel straightening involves using various hand tools and equipment to force the panel back into its original shape. Body filler is used to cover any small dents remaining in the worked panel. The vehicle is sanded and cleaned to prepare surfaces for the painting process.
Masking is done to cover areas that will not be painted. Priming is done to cover bare metal before painting. The mixing room or mixing lab is a power-ventilated area where refinish materials are mixed or prepared for application.
The vehicle’s paint or finish performs two basic functions—it beautifies and it protects.
Refinishing or repainting involves the steps needed to properly restore the vehicle’s finish (paint).

## Slide 37
Summary
The primecoat is used to improve adhesion (sticking) of the topcoat. The terms topcoat and colorcoat refer to the paint applied over the primecoat. Basecoat/clearcoat paint systems use a colorcoat applied over the primer-sealer with a second layer of transparent clearcoat over the colorcoat.
Spraying involves using precision paint spray guns and a spray booth to apply refinish materials to the car body. A spray gun uses compressed air to break the liquid paint into a fine mist so that the paint is deposited smoothly on the vehicle body.
The paint booth is a clean room with filtered air circulation so that dirt does not get into the paint when spraying. In the drying room, infrared lights are used to speed up the paint curing or drying process by warming the paint.

## Slide 38
Summary
A detailer performs all the last tasks needed to prepare the vehicle for return to the customer.
Auto body technicians are skilled people who know how to use specialized equipment and highly technical methods to restore severely damaged vehicles.
The term professional refers to the attitude, work quality, and image that a business and its workers project to customers.