## Slide 1: Electrical/Electronic System Operation and Service
Chapter 22
Notes: 1

## Slide 2
FIGURE 22–10 During a collision, wires can be smashed and shorted. You or a specialized electrical technician must find and correct wiring problems during collision repair.

## Slide 3: Objectives
Explain basic electrical values: volts, ohms, and amps
Use Ohm’s Law to calculate circuit values
Describe the difference between series and parallel circuits
Describe the test procedures used to repair electrical and electronic systems
Repair vehicle wiring harnesses damaged during a collision
Notes: 3

## Slide 4: Objectives (continued)
Use a scan tool to check for electrical troubles before and after collision repairs
Replace damaged computer system components
Connect and use a multimeter to perform basic electrical tests
Correctly answer ASE-style review questions relating to electrical/electronic systems
Notes: 4

## Slide 5: Introduction
Electrical repairs
  Repairing severed wiring, replacing engine sensors, scanning for computer or wiring problems, etc.
Collision can easily crush vehicle’s wires and electrical components
Most modern vehicle mechanical systems are monitored or controlled by on-board computers
Notes: 5

## Slide 6: Electrical Terminology
Current: movement of electricity (electrons) through a wire or circuit
  Direct current (DC)
  Alternating current (AC)
Voltage: pressure that pushes electricity through wire or circuit
Resistance: restriction or obstacle to current flow
Conductor: carries current to parts of a circuit

## Slide 7: Electrical Terminology (continued)
Ohm’s law
  Mathematical formula for calculating an unknown electrical value (amps, volts, or ohms) when two values are known
Magnetism
  Study of how electrical fields act on ferrous (iron-containing) objects
  Flux or magnetic field
    Present around permanent magnets and current-carrying wires

## Slide 8: Electrical Terminology (continued)
Electric circuits
  Contain a power source, conductors, and a load
  Series circuit
  Parallel circuit
  Series-parallel circuit

## Slide 9
FIGURE 22–3 Most circuits in a car or truck are frame ground circuits. The frame or unibody is used to return electrical current to the battery. This reduces the amount of wires needed to complete circuits. Note ground symbols.

## Slide 10
FIGURE 22–4 Compare basic series and parallel circuits. (A) With a series circuit, if one lightbulb or load burns out, the whole circuit will stop working. (B) With a parallel circuit, other legs of the circuit will keep it working if one bulb or load burns out.

## Slide 11: Electrical Terminology (continued)
Wiring diagrams, schematics, and trees
  Wiring diagram: graphic representation of all parts and wires in a circuit
  Electrical abbreviations
  Electrical symbols
  Wire color coding
  Wiring harness

## Slide 12
FIGURE 22–9 When disconnecting electrical connectors, be careful not to damage them. You might have to lift a small tab, insert a pointed tool, or squeeze the connector together to release and disconnect it.

## Slide 13: Checking Electrical Problems
Vehicle’s wiring harnesses route wires from battery to all electrical components
Collision forces can pull wires from their connections
Corrosion damage can loosen ground wire connections, breaking electrical circuits
Follow manufacturer’s recommendations when repairing wiring harness damage

## Slide 14
FIGURE 22–11 Note the basic steps for repairing an individual wire using a crimp and solder connector. (A) Cut away the smashed area of wire. Strip off a short piece of plastic insulation. Slide a heat shrink tube over the wire. (B) Insert the wires into the metal crimp connector. Use electrical pliers to crush the connector down over the stripped wire ends. (C) Use a soldering gun to solder the wires and connector together. (D) Slide the heat shrink tube down over the connector. Heat it with a heat gun. The plastic will melt and shrink down over the connector.

## Slide 15: Checking Electrical Problems (continued)
Open circuits
  Disconnected circuit
  Does not have a complete electrical path
Short circuits
  Unwanted path for electrical current
  Dead short to ground
  Intermittent short
  Cross circuit short
  High-resistance short to ground

## Slide 16: Battery
Stores electrical energy as chemical energy
Always disconnect the battery ground cable as soon as vehicle is received at shop
Precautions that must be taken when recharging a battery

## Slide 17: Battery (continued)
Using jumper cables
  Jumper cables may be needed to start engine in order to bring vehicle into shop
  Procedure for using jumper cables
  Precautions to avoid damage from voltage spikes in electronic circuits of a vehicle with a dead battery

## Slide 18: Electrical Diagnostic Equipment
Testlight and jumper wires
  Externally powered testlight
    Often used to determine whether there is a complete, unbroken circuit
    If lamp lights, current is flowing through circuit
  Jumper wires
    Temporarily bypass circuits or components for testing
    Test circuit breakers, relays, lights, and other components

## Slide 19
FIGURE 22–21 Here jumper wires are being used to check for a bad ground wire. If the bulb starts working with the jumper, you have found high circuit resistance or an open in the ground circuit.

## Slide 20: Electrical Diagnostic Equipment (continued)
Multimeters
  Voltmeter, ohmmeter, and ammeter combined into one case
  Measure actual electrical values for comparison to known good values
  Also called volt-ohm-ammeter (VOM)
  Digital multimeter (DVOM)
  Analog multimeter

## Slide 21
FIGURE 22–22 A multimeter is an important tool for today’s repair technician. It reads voltage, current, and resistance.

## Slide 22: Electrical Diagnostic Equipment (continued)
Measuring resistance
  Always disconnect circuit from power source
  General procedure to measure resistance
Measuring voltage
  Multimeters allow you to select alternating current voltage (ACV) or direct current voltage (DCV)
  When using multimeters to measure voltage, selection of the range scale is very important

## Slide 23
FIGURE 22–24 Note the various checks that can be made with a multimeter to determine taillight circuit problems. This type of analysis also applies to other types of circuits. (A) Check for power to the fuse panel. (B) Check for voltage after the main switch and fuse. (C) Check for voltage at taillight sockets. (D) An ohmmeter will check for grounds at taillights.

## Slide 24: Electrical Diagnostic Equipment (continued)
Measuring current
  Current or amperage measured to check consumption of power by a load
  Measuring current in modern ammeters
  Measuring current in older ammeters
  High-current draw indicates low resistance
    Dragging or partially shorted motor
  Low-current draw means high resistance
    Bad connection or dirty motor brushes

## Slide 25: Electric Components
Switch: turns circuit on or off manually
Solenoid: electromagnet with movable core or plunger
Relay: remote control switch
Inertia switch: designed to shut electric fuel pump off after a collision
Motors: use permanent magnets and electromagnets to convert electrical energy into a rotation motion for doing work

## Slide 26
FIGURE 22–26 This illustration shows the electrical components found in the engine bay of one vehicle. During a hard frontal collision, these parts can be smashed and damaged, requiring replacement.

## Slide 27: Circuit Protective Devices
Prevent excess current from burning wires and components
Fuse box (or fuse panel) holds circuit fuses, breakers, and sometimes flasher units for turn and emergency lights
Fuses
  Burn in half with excess current to protect a circuit from further damage
  Fuse ratings: current at which fuse will blow

## Slide 28: Circuit Protective Devices (continued)
Fuse links
  Smaller diameter wires spliced into the larger circuit wiring for overcurrent protection
  Also called fusible links
Circuit breakers
  Heat up and open with excess current to protect circuit
  Cycling circuit breakers
  Noncycling circuit breakers

## Slide 29
FIGURE 22–33 A circuit breaker uses a bimetal arm that bends with heat-generated current flow. If the current goes too high, heating of the bimetal arm causes it to bend and open circuit contacts. When the bimetal arm cools, it bends back to reconnect the circuit.

## Slide 30: Lighting and Other Electrical Circuits
Automotive lighting systems have become increasingly sophisticated
Headlight assemblies often damaged in frontal collisions
Aiming headlights
  Inspections that should be made before making adjustments to headlights
  Headlight aimers: for adjusting headlights to shine at proper height and side direction in front of vehicle

## Slide 31
FIGURE 22–38 Note how the shop wall and floor have been marked for aiming headlights. Pull a vehicle up to the line drawn 25 feet from the wall. Measure the headlight heights, the width between bulbs, and the centerline. Draw lines on the wall or mark them with masking tape. When the headlights are turned on, they should hit the wall on your alignment marks.

## Slide 32: Lighting and Other Electrical Circuits (continued)
Tail, backup, and stoplights
  Failure of tail, backup, stop, or directional light usually attributed to faulty bulb
  Moisture getting into bulb socket causes corrosion of electrical contacts and bulb
Windshield wipers and washers
Horn
  Most horn systems use steering wheel switch and relay for sounding the horn

## Slide 33
FIGURE 22–42 This is a typical configuration of windshield wipers and washers. The wiper motor normally attaches to the firewall, either in the engine compartment or under the dash. The washer bottle is often cracked during frontal collisions and should be inspected for leakage and normal operation.

## Slide 34: Lighting and Other Electrical Circuits (continued)
Starting and charging systems
  Starting system
    Large electric motor turns engine flywheel
    This spins, or “cranks,” crankshaft until engine starts and runs on its own power
  Charging system
    Recharges battery and supplies electrical energy when engine is running

## Slide 35: Lighting and Other Electrical Circuits (continued)
Electrical troubleshooting charts
  Provide diagnostic procedures that are read from top to bottom in a specific sequence
Battery drain
  Causes current to flow out of battery when everything should be off
Engine no-start
  If an engine cranks but fails to start, check for “spark” and “fuel”

## Slide 36: Electronic System Service
Many electronic diagnostic and repair procedures are not that difficult
Technicians can find and fix many electronic problems by:
  Going back to basics of electrical circuits
  Following few simple rules
Knowledge of electronics is necessary for technicians to perform their jobs

## Slide 37: Electronic Displays
In collision repair, electronic displays call for special cautions
Most dashboard gauges are driven by some type of electrical signal
  Gauges can either be analog or digital
Digital displays
Analog displays

## Slide 38
FIGURE 22–50 (A) An analog display has gauge needles that sweep around. (B) A digital display has number displays and sometimes analog indicators that move or slide across to show vehicle speed, for example.

## Slide 39: Electronic Displays (continued)
Display types
  Light-emitting diode (LED)
  Liquid crystal diode (LCD)
  Vacuum fluorescent diode (VFD)
Air bags
  Air bag system uses impact sensors, vehicle’s on-board computer, inflation module, and nylon balloon in steering column to protect driver during a head-on collision

## Slide 40: Computer Systems
Almost all vehicle systems are now controlled by computer
Basic computer system consists of:
  Sensors (input devices)
  Actuators (output devices)
  Computer (electronic control unit)
Antilock brakes
  Antilock brake system (ABS): electronic/hydraulic “pumping” of brakes for straight line stopping under panic conditions

## Slide 41
FIGURE 22–51 Computers, also called electronic control modules, can be found throughout the vehicle. When doing body repairs that require welding, computers should be protected from heat or removed.

## Slide 42: Computer Systems (continued)
Computerized suspension
  Uses sensors and electronic control unit to adjust height, leveling of car, and ride firmness
Computer-assisted steering
  Electric motor replaces hydraulic pump, hoses, and fluid associated with conventional power steering systems
On-board diagnostics (OBD)
  Computer system can detect its own problems
  On-board diagnostics II (OBDII) systems

## Slide 43: Computer Systems (continued)
Scan tool use
  Scan tool: electronic instrument for reading trouble codes and converting them into problem explanations
  Four categories of OBDII trouble codes
Computer problems
  PROM: programmable read-only memory chip mounted in computer
    May need to install from old computer to new computer when replacing a computer

## Slide 44: Computer Systems (continued)
Protecting electronic systems
  Procedures to protect automotive electrical systems and electronic components during storage and repair

## Slide 45: Summary
Electrical repairs include tasks such as repairing severed wiring, replacing engine sensors, and scanning for computer or wiring problems.
Current is the movement of (electrons) electricity through a wire or circuit.
Voltage is the pressure that pushes electricity through the wire or circuit.
Resistance is a restriction or obstacle to current flow. It tries to stop the current caused by the applied voltage.
An open circuit is disconnected and does not have a complete electrical path.

## Slide 46: Summary
A short circuit has an unwanted current path. A collision will sometimes create a short circuit.
If an engine cranks but fails to start, check for “spark” and “fuel.”
A conductor carries current to the parts of a circuit.
“Hot” wires connect the battery positive to the components of each circuit.
Insulation stops current flow and keeps current in the metal wire conductor.
A frame ground circuit uses the metal body as a return wire to the negative terminal of the battery.

## Slide 47: Summary
A series circuit has only one conductor path, or leg, for current through the circuit.
A parallel circuit has two or more legs, or paths, for current.
A wiring diagram is a graphic representation of all parts and wires in the circuit.
Electrical symbols are graphic representations of electrical/electronic components.
Wire color coding allows you to find a specific wire in a harness or in a connector.

## Slide 48: Summary
A wiring harness has several wires enclosed in a protective covering.
The battery stores electrical energy as chemical energy. Improper handling of batteries can cause severe acid burns, and ignited gas can cause the battery to explode.
A multimeter is a voltmeter, ohmmeter, and ammeter combined into one case.
A solenoid is an electromagnet with a movable core or plunger. When energized, the plunger is pulled into the magnetic field to produce motion.

## Slide 49: Summary
A relay is a remote control switch.
A fuse box holds the various circuit fuses, breakers, and sometimes the flasher units for the turn and emergency lights.
Fuses burn in half with excess current to protect a circuit from further damage.
A fuse link, or fusible link, is a smaller diameter wire spliced into larger circuit wiring for overcurrent protection.

## Slide 50: Summary
Circuit breakers heat up and open with excess current to protect the circuit. They do not suffer internal damage like a fuse.
The starting system has a large electric motor that turns the engine flywheel.
The charging system recharges the battery and supplies electrical energy when the engine is running.
A battery drain is a problem that causes current to flow out of the battery when everything should be off.

## Slide 51: Summary
Sensors are devices that convert a condition (temperature, pressure, part movement, and so on) into an electrical signal.
Actuators are devices (solenoids or servo motors, for example) that move when responding to electrical signals from the computer.
A computer is a complex electronic circuit that produces a known electrical output after analyzing electrical inputs.

## Slide 52: Summary
Modern antilock brake systems (ABS) can be thought of as electronic/hydraulic “pumping” of the brakes for straight-line stopping under panic conditions.
On-board diagnostics (OBD) means the computer system can detect its own problems.
A scan tool can convert the computer number code into an explanation of the problem.